## Slide 1
HACKATHON PROTOTYPE · 24-HOUR BUILD
Guiding Mine Vehicles
Around Temporary Hazards
A low-visibility hazard-awareness and reroute system for open-cast mine haul roads — reframed from our SIH mine-vehicle safety concept.
Reference site: NMDC Bailadila, Chhattisgarh (open-cast, iron ore)
59%
of fatal accidents in Indian opencast coal mines are caused by dumpers alone
Source: DGMS data (1995-2008), analysed in peer-reviewed opencast mobile-machinery accident study
Team Nexo · SIH-reframed prototype
Guiding Mine Vehicles Around Temporary Hazards

## Slide 2
WHY
The problem is real, specific, and vehicle-centric
59%
of fatal accidents in Indian opencast coal mines are caused by dumpers
DGMS data, 1995-2008
1st
documented cause: fog directly reduces haul-road visibility, increasing collision risk
Opencast mining safety literature
54
haul-truck fatalities studied by NIOSH specifically to justify collision-warning systems
CDC/NIOSH, 2005-2021
An official DGMS circular documents real case examples that match our exact hazard model: an engine stalling on a ramp leading to rollback and fatality, and a dumper-to-dumper collision on a haul road.
Sources listed in full on the accompanying 5W1H spreadsheet
Guiding Mine Vehicles Around Temporary Hazards

## Slide 3
OUR FRAMING
Why a STALLED vehicle — not a static rock — is the hazard
Static obstacle
(e.g. a rock)
Stalled vehicle
(our chosen signal)
Always present — not a temporary hazard, doesn't fit the PS framing
Solved locally by a vehicle's own ultrasonic sensor — sharing its location to other vehicles adds nothing
No reroute is actually needed — just local stop/avoid
Genuinely temporary — blocks a path segment only until cleared, matches "normally safe, temporarily hazardous"
Blocks the full path for every vehicle behind it — a real reroute-worthy event
Detected via motor-on + wheel-encoder showing no movement — unambiguous, reproducible on demand
Chosen signal maps directly onto the PS's own language: “temporarily dangerous, normally safe path”
Guiding Mine Vehicles Around Temporary Hazards

## Slide 4
HOW IT WORKS
Three-layer architecture
1
SENSING
MPU6050 · Wheel Encoder · Ultrasonic · ESP32-S3
Each vehicle detects its own hazard events locally: stall, tilt, obstruction.
→
2
MESH
WiFi / ESP-NOW → Raspberry Pi 5
Hazard events broadcast from the vehicle (and phone-simulated second node) to the base station.
→
3
ROUTING
Go backend · Route graph · Dashboard
On a hazard event, the blocked edge's weight spikes; shortest path recomputes; other vehicles reroute.
No GPS/LoRa/radar available for this build — mesh runs over WiFi, positioning is encoder+gyro dead-reckoning
Guiding Mine Vehicles Around Temporary Hazards

## Slide 5
DETECTION LOGIC
How a stall event actually fires
1
Motor commanded ON
Vehicle is instructed to move forward
→
2
Encoder shows ≈ 0 movement
Wheel isn't rotating despite the command — physically blocked
→
3
Condition holds ≥ 2 seconds
Debounce window filters out normal bumps and brief stops
→
4
STALLED event fires
Position + vehicle ID broadcast to base station
Position tracking: real encoder + gyro dead-reckoning odometry (distance from wheel encoder, heading from MPU6050 gyro integration) — not GPS. Single-wheel encoder means no differential-odometry fallback, so heading depends entirely on the gyro and will drift over long runs. Named as a known limitation with an RTK/dual-encoder upgrade path (see spreadsheet).
Wheel-slip (wheel spinning, chassis stationary) is a known, unclosed gap — flagged, not solved, in this build
Guiding Mine Vehicles Around Temporary Hazards

## Slide 6
LIVE DEMO
Backup video available if live hardware has issues
Vehicle stalls → hazard broadcast → dashboard reroutes second node in real time
Guiding Mine Vehicles Around Temporary Hazards

## Slide 7
HONEST LIMITATIONS
Known constraints — and the costed upgrade path
Prototype constraint
Production upgrade
Single wheel encoder
Dual-wheel differential odometry
No GPS/RTK
RTK-corrected GPS, sub-meter accuracy
Ultrasonic (~4m range)
mmWave radar — sees through fog/dust
WiFi/ESP-NOW (~tens of metres)
LoRa mesh — kilometre range
Per-vehicle sensing cost (USD, approx.)
Chart: USD
| Position Sensing | Obstacle Sensing | Comms | Compute
Prototype (USD) | 7 | 4 | 0 | 8
Production (USD) | 210 | 240 | 15 | 8
Full BOM detail and sourcing in the accompanying spreadsheet
Guiding Mine Vehicles Around Temporary Hazards

## Slide 8
IMPACT
Who this helps, and what comes next
Vehicle operators
Direct safety — warned before entering a blocked segment
Control room / safety officers
Real-time visibility into fleet-wide hazard state
Mine operators
Reduced downtime and liability exposure from haul-road incidents
This is a limited proof of concept, built with the sensors we had budget for in 24 hours. With production-grade sensing — RTK GPS, LoRa, mmWave radar — the same architecture scales to a full open-cast haul-road deployment.
Thank you
Team Nexo — Guiding Mine Vehicles Around Temporary Hazards
Prototype and evidence base available in the accompanying spreadsheet
Guiding Mine Vehicles Around Temporary Hazards